## Slide 1: SYSTEM ARCHITECTURE DESIGN OF THE ASPIRE 2A SYSTEM
26 July 2022
Paul HIEW
Senior Systems Manager, Tech Operation
(Solution Architect of ASPIRE2A)
contact@nscc.sg
23 July 2021 20:03pm – Paul Hiew
Notes: 23 July 2021 20:03pm – Paul Hiew

## Slide 2
CURRENT
IN DEVELOPMENT
FUTURE
1 PFLOP (2016) to 10-20 PFLOPS (2025)
~10-20 PFLOPS Capacity
Note: Floating-point operations per second, or FLOPS, is a measure of compute performance or how quickly and effectively a computer works. P or peta (used in units of measurement) denotes a factor of 1015. The Top 500 supercomputers today are minimally in the PFLOPS range.
Add-on Systems (ASPIRE 1+)
AI.Platform (6 x DGX-1)
1,000 cores HTC System
Koppen - 160 TFLOPS Cray XC-50, Climate System
In Progress
Aggregate ~10PFLOPS raw compute power
8x more powerful than current ASPIRE1
Notes: FOR GENERAL audience

## Slide 3: Superconnected Locally - Ultra High-speed InfiniBand for Data Transfers
Leveraging long-haul InfiniBand switches, NSCC is able to deliver high-bandwidth and low-latency between different geographic locations in Singapore. Our connections are done in collaboration with the Singapore Advanced Research and Education Network (SingAREN) and SingAREN-Lightwave Internet Exchange (SLIX).
This means that researchers using ASPIRE1 at locations islandwide experience the same connectivity and speed as if they were at NSCC itself!
National Supercomputing Centre Singapore (NSCC)
Our current connections link:
Agency for Science, Technology and Research (A*STAR)
National University of Singapore (NUS)
Nanyang Technological University (NTU)
Singapore University of Technology and Design (SUTD)
With more connections to come!
Notes: FOR GENERAL audience

## Slide 4
Notes: FOR GENERAL audience

## Slide 5
Narinder Kapoor – GM & SVP APAC
Nick Gorga GM HPC & AI APAC/India

## Slide 6
105,984 Cores
CPU (AMD EPYCTM 7713)
800 Nodes
1,024 Cores
High Frequency Nodes (AMD EPYCTM 75F3)
16 Nodes
352 GPUs
Accelerated Nodes
GPU (NVIDIA A100)
82 Nodes
476 TB
Total System Memory
25 PBytes
Storage (Spinning + Nearline)
10 PBytes
Scratch Disk
Advanced Supercomputer for Petascale Innovation Research & Enterprise
- Singapore’s newest supercomputer providing HPC resources for local research
2A
ASPIRE 1
Singapore’s first national petascale supercomputer
more Cores
>3.5x
more Compact
5x
1.5x less Nodes
more GPUs
2x
Compute Power
8x
ASPIRE2A Overview

## Slide 7: Summary of Hardware Specification
Total CPU Nodes : 800
    High Frequency Nodes : 16
Total Accelerated Nodes : 82
Total number of cores:
    7713 : 105,984
    75F3 : 1,024
Total Memory : 476 TB
Total GPU (A100) : 352
Total Storage:
    Persistent : 10 PB (spinning)
      +
      15PB (nearline)
    Scratch : Approximate 10 PB

## Slide 8: Simplified Floor Plan (not according to scale)
NUS-i4
* Subject to change
Area B
Area A
Power consumption approximately 800kW*
FRONT
CDU
CDU
Main System
+ 2TB Largemem nodes
+ Type A Accelerated Nodes
Power consumption approximately 270 kW*
Row A
1
2
3
Storage (GPFS, Lustre & DMF)
+ Administrative servers
+ MISC
+ 4TB Lagemem nodes
+ Type B & Type C Accelerated Nodes
+ HFN
Row B
4
5
6
Notes: Detail will be present by Colleague during next slides.
Lustre - Scratch/Buffer
IBM SpectrumScale (GPFS) - Project/Home
HPE Data Management Framework (HPE DMF)
Compute - 12 x Quad GPU nodes, 6xOcta GPU nodes, 4x 4TB Largemem Nodes 16x High Frequency Nods
Management Switches
Administrative and Misc - HCI-Login-Viz

## Slide 9
CrayEX
768 nodes
Dual sockets
AMD EPYC 7713, 512GB RAM
  Base Speed 2.0GHz – 3.14 PFLOPS (Rpeak)
  Boost 3.7GHz – 5.81 PFLOPs (Rpeak)
CrayEX Large Memory Nodes Type 1:
12 nodes
Dual sockets
AMD EPYC 7713, 2048GB RAM
  Base Speed 2.0GHz – 0.05 PFLOPS (Rpeak)
  Boost 3.7GHz – 0.09 PFLOPs (Rpeak)
Large Memory Nodes Type 2 :
4 nodes
Dual sockets
AMD EPYC 7713, 4096GB RAM
  Base Speed 2.0GHz – 0.01 PFLOPS (Rpeak)
  Boost 3.7GHz – 0.03 PFLOPs (Rpeak)
CrayEX GPU Nodes Type 1:
64 nodes
Single socket
AMD EPYC 7713, 512GB RAM
  Base Speed 2.0GHz – 0.13 PFLOPS (Rpeak)
  Boost 3.7GHz – 0.24 PFLOPs (Rpeak)
4 x NVIDIA A100-40G SXM per node
  Raw Peak AI -- 159.74 PFLOPS
GPU Nodes Type 1:
12 nodes
Single socket
AMD EPYC 7713, 512GB RAM
  Base Speed 2.0GHz – 0.02 PFLOPS (Rpeak)
  Boost 3.7GHz – 0.04 PFLOPs (Rpeak)
4 x NVIDIA A100-40G SXM per node
  Raw Peak AI -- 29.95 PFLOPS
GPU Nodes Type 2:
6 nodes
Dual sockets
AMD EPYC 7713, 1024GB RAM
  Base Speed 2.0GHz – 0.02 PFLOPS (Rpeak)
  Boost 3.7GHz – 0.04 PFLOPs (Rpeak)
8 x NVIDIA A100-40G SXM per node
  Raw Peak AI -- 29.95 PFLOPS
High Frequency Nodes :
i) 16 nodes
Dual sockets
AMD EPYC 75F3, 512GB RAM
  Base Speed 2.9GHz – 0.05 PFLOPS (Rpeak)
  Boost 4.0GHz – 0.06 PFLOPS (Rpeak)
Area A
Area B

## Slide 10: General Hardware Specification
Main System: 768 nodes (98,304 cores) (Rpeak:3.145 PFLOPS; Rmax:2.52 PFLOPS)
Each nodes 2x AMD EPYC Millan 7713
          Base clock @ 2.0GHz
          Max Boost Clock @ Up to 3.675GHz
          64 cores each socket (128 cores per node)
          Total L3 Cache @ 256MB
          TDP 225W
    Each nodes 8 channels DDR 4, 3200, 512GB RAM
Large Memory Nodes: 16 (12 + 4) nodes (2,048 cores)
2TB nodes (12): Each nodes 2x AMD EPYC Millan 7713 (128 cores per node)
4TB nodes (4): Each nodes 2x AMD EPYC Millan 7713 (128 cores per node)
Area A
Cont.
Area B

## Slide 11: General Hardware Specification (cont.)
High Frequency Node (HFN): 16 (12 + 4) nodes (1,024 cores)
Each nodes 2x AMD EPYC Millan 75F3
          Base clock @ 3.2GHz
          Max Boost Clock @ Up to 4.0 GHz
          32 cores each socket (64 cores per node)
          L3 Cache @ 256MB
          TDP 280W
    Each nodes 8 channels DDR 4, 3200, 512GB RAM
Accelerated Nodes: 82(64 + 12 + 6) nodes (5,632 cores), 352 units of NVIDIA A100
- 8 channels DDR 4, 3200
- NVIDIA A100 40GB
Type A (64): Each nodes 1x AMD EPYC Millan 7713 512GB (64 cores per node)
Rpeak:0.131 PFLOPS – CPU
Rpeak:4.99 PFLOPS – GPU
(Raw Peak AI): 159.74 PFLOPS
Type B (12): Each nodes 1x AMD EPYC Millan 7713 512GB (64 cores per node)
Type C (6): Each Nodes 2x AMD EPYC Millan 7713 1024GB (128 cores per node)
Area A
Area B

## Slide 12
Area A, Cray EX
Main-System : 768 nodes
Large Memory Nodes: 12 nodes (2TB per node)
Accelerated Nodes : 64 nodes (4x A100 GPU per node)
CDU

## Slide 13
Area A | Cray EX Compute Cabinet Layout

## Slide 14
Area A | Cray EX Compute Cabinet Layout

## Slide 15
Area A | Cray EX Compute Blade

## Slide 16
HPE Slingshot switch for the HPE Cray EX liquid-cooled system
HPE Slingshot top of rack switch for air-cooled HPE Cray Supercomputers
HPC| HPE Slingshot Switch

## Slide 17
Login, Viz, Specialized Compute & Storage Partition (Class 2)
Cray EX - Base Compute Partition (Class 4)
Dragonfly Topology
11 TB/s Injection b/w
6.4 TB/s Global b/w
>50% global b/w taper
Cabinet 1
Cabinet 4
Cabinet 2
Cabinet 3
Area A
Compute & Storage Racks
Bundle Size = 8
2 x Edge Switch
2 x Edge Switch
HCI (Altair)
HCI (DMZ)
1 x Edge Switch
Injection ports -282 Injection b/w – 7.05TB/s Global b/w – 3.6TB/s >50% global b/w taper Bundle size = 2
Login, Viz, Specialized Compute are in 1 row. 2 groups of switches.
Storage is in a 2nd rack row. 4 groups of switches.
HCI access to Slingshot via Edge Switches
Bundle Size =4 2.4 TB/s
HPC| Slingshot Design
Area B

## Slide 18
Slingshot Fabric with HPE Cray EX Cabinet (Group)
16x CPU nodes
w/ single-rail 100 Gbps
8x GPU nodes
w/ dual-rail 100 Gbps
400 Gbps-per link
Group
(Cabinet)

## Slide 19
Slingshot Fabric with HPE Cray EX Cabinet (Group)
Zoom In
12
13
00
01
02
03
04
05
10
11
15
14
06
07
08
09
16nodes
per switch
Slingshot switch

## Slide 20: Software Environment
System
Development
Red Hat
Enterprise Linux 8
GPFS
Lustre
Altair Access
Altair PBS Pro
*Kubernetes with Docker
GNU GCC
AMD AOCC
Intel oneAPI
Nvidia CUDA
NVHPC
Profiling & Debugging
ARM Forge
Cray Stat
gdb4hpc
Valgrind4hpc
Perftools
Application
Library
Cray MPICH
OpenMPI
AMD AOCL
Cray LibSci
FFTW
GSL
Intel MKL
PETSc
HDF5
NetCDF
Java
Julia
Octave
Python
R
Anaconda3
Tmod
RELION
MRtrix3
GNU Parallel
Cylc
Rose
Nextflow
ABySS
BEAST
bedtools
BLAST+
bowtie2
GATK
BWA
SAMtools
BerkeleyGW
GROMACS
LAMMPS
Mumax3
OpenFOAM
Nek5000
Nektar++
Quantum ESPRESSO
WRF
Tensorflow
PyTorch
FCM
HPE CCE
Operating System
Parallel File System
Container
Singularity
Workload Manager
Cray Programming Environment
Programming
I/O Libraries
Scientific Libraries
MPI Libraries
Workflow
Bio Tools
AI
Simulation
Applications and Tools
Go
BLIS
Velvet
Ncview
NCL
FFmpeg
Remote Visualization
Officially supported software on ASPIRE1 : 151*
Out of the topmost** active 20 software (Jan-Jul 2022), 83.33% is ready on ASPIRE2A
*Include old version, since 2016
** Officially supported by NSCC

## Slide 21
Compute Resources (HPC, AI, HTC and etc)
Tape
Object Storage & Cloud
Zero Watt Storage
Software
Defined
Storage
High-Performance Storage
XFS
Tier Zero
Lustre
Spectrum Scale
(GPFS)
HPE Data Management Framework
Metadata management & data provenance
Policy-based data migration with job scheduler integration
Data protection, repair and disaster recovery
Data Management Framework

## Slide 22: General Hardware Specification
persistent
GPFS(approximate 8PB):
- Flash: r210GB/s, w119GB/s
- HDD: r56GB/s, w46GB/s
By policy
Storage:
scratch
Lustre (approximate 10PB): (current 3PB)
- Flash: r440GB/s, w320GB/s
- HDD: rw150GB/s
nearline
DMF (15PB+20PB):
- ZeroWatt Storage (ZWS), 40GB/s
- 40Gb/s pipe over stage 8GB/s to tape
Warm
Cold

## Slide 23
Entire namespace is available in the filesystem
Migrate file data transparently (with invisible IO), leaves inodes
Recall on access or by schedule
Primary Storage (POSIX)
Online, high-performance disk
Flash-based storage tier
Lustre, GPFS or HPE XFS
Automated Data Migration
Automated Data Recall
Nearline Fast-Mount Cache
High capacity, low cost HDD
Direct power-managed disk
DMF ZeroWatt Storage (ZWS)
Deep Storage
Object Store (S3)
Public Cloud (S3)
Tape
Data Management | DMF Core Concepts
Notes: Very helpful to understand fundamental mechanisms in use by HPC Data Management Systems

## Slide 24
NSCC Facility
20 PB
Tape Archive
DMF GPFS HSM
GPFS is policy protected by DMF for backup & active archive (Nov 2019) DMF natively manages GPFS with direct parallel data streams to tape
Lustre
3.56 PB
40GB/s
DMFv7
Lustre (1 PB)
(/seq)
Persistent Namespace
Manual failback after DR
ABCP Solution
3.56 PB @ 40 GB/s Primary Disk (aggregate)
20PB @ 6 GB/s Tape (aggregate)
Lustre HSM
DMF natively manages Lustre data with direct parallel I/O to tape.
DB Servers
&
Data Movers
Lustre HSM
DMF natively manages Lustre data with direct parallel I/O to tape.
LDAP Server
LDAP Server
LDAP Mirror
Data Restoration
DMF can recall data to local or remote DMF managed filesystems irrespective of source filesystem.
GPFS
9 PB
3x filesystems
(/home, /data and /secure)
ABCP Storage Fabric
Computational
Cluster
LNET
Router
Data Management | DMF Design Overview

## Slide 25
Lustre
3.56 PB
40GB/s
DMFv7
Persistent Namespace
ABCP Solution
3.56 PB @ 40 GB/s Primary Disk (aggregate)
20PB @ 6 GB/s Tape (aggregate)
20 PB
Tape Archive
Data Movers
LDAP Server
LDAP Mirror
NSCC Facility
Lustre
1 PB
(/seq)
LDAP Server
GPFS
9 PB
3x filesystems
(/home, /data and /secure)
ABCP Storage Fabric
Computational
Cluster
LNET
Router
NSCC new Facility
For future expansion
/projects
/home
. . .
LDAP Server
DB Servers
&
Data Movers
ZWS
Logical Flow of Data
Logical Flow of Data
Data Management | DMF Design Overview
Notes: Currently we have Aspire1 main storage data (/home, /data, /secure and /seq) being backup using DMF to NTU via the long distance InfiniBand (IB).
Moving forward, at NUS i4 the new faculty, we like the vendor’s proposed storages/volume to be connected to DMF and leverage its HSM capability.
Thus the vendor also need to provide the new sizing and tiering at NTU.

## Slide 26
GPFS
lustre
GPFS
Vicinity
PL2000AD
PL2000AD
Vicinity
Tape
Db
x7
Data mover
x4
Lustre
ZWS
Mellanox
Mellanox
Mellanox
Mellanox
Mellanox
Mellanox
Mellanox
FC
Slingshot
Db
x11
Data mover
x2
ZWS
Data mover
x2
NTU’s ASP1 login + Load balancing nodes
(4+2)
New
1
2
3
1
2
ASP1 -> NTU’s Tape (1st copy)
ASP1 – route NTU-> i4’s ZWS (2nd copy)
ASP2 -> i4’s ZWS -> NTU’s Tape
1
2
ASP1 – route NTU-> i4’s ZWS -> NTU’s Tape
1
2
3
1
2
ASP1’s GPFS
ASP2A’s GPFS
ASP1
ASP2A
stage
Extend ASP1’s IB Fabrics to DMF

## Slide 27
As of 24 Feb 2022
Example for the Filesystem usage:
Notes: Average 14.92%
For 1st FS, we just need 45% to cater for 1 year
For 2nd FS, we need 60% to cater for 1 year

## Slide 28: Call for Early Use of ASPIRE 2A
Application Period: 1 Aug 2022 to 30 Nov 2022 (subject to changes)
Resource Allocation Period: Starting from Q4-2022
  NSCC will be accepting applications while getting the system ready. Once the system is ready, we will inform all successful applicants on the onboarding process
This call is open for the early use of ASPIRE 2A for purposes such as software verification, porting, tuning, test runs, etc.
Applicants will be notified of the outcome via email as soon as the review process is completed.
For users with existing projects, the project data will be migrated from ASPIRE 1 to ASPIRE 2A. Once the project is successfully running on ASPIRE 2A, it will cease to run on ASPIRE 1.
Applications can be submitted via the Online Application Form.

## Slide 29
Unloading
Checking Order
Floor Boarding outside DC
In Area A
In Area B(before floor protection)
Updates on IT Equipment Delivery (15-16 Nov)
Notes: Here are some visuals from the first delivery that took place last week

## Slide 30
Usage of Server Lifter to lift and mount the D8000 enclosures
Updates on IT Equipment Delivery

## Slide 31
D8000 HDD on pallet
Unpacking HDD to be slotted into D8000 enclosure
In progress of slotting HDD into D8000 enclosure
Updates on IT Equipment Delivery on 28 DEC (D8000 HDD)

## Slide 32
Walk through with CrayEX mock-up
Wooden box and pallet jack @ Area A
Eg of servers mounted in Row A, Area B
Updates on IT Equipment Delivery

## Slide 33
Lifting of Dry Cooler Structure on 21 Dec

## Slide 34
Lifting of Dry Cooler
Dry Cooler and Structure in position
Dry Cooler Delivery on 23 Dec

## Slide 35
Updates on IT Equipment Delivery
Arrival of 1 unit of CrayEX and CDU on 8 Feb
Notes: Here are some visuals of CrayEX delivery last week on 8 Feb.

## Slide 36
Updates on IT Equipment Delivery
Arrival and set up of remaining CrayEX + CDU on 23 Mar
Notes: If you’ve not been to the DC.. This is

## Slide 37
ASPIRE2A

## Slide 38: Thank You for Your Attention

## Slide 39: Fun Facts ASP2A vs ASP1
3.54 times more cores
1.5 times less nodes
  5 times more compact
2 times more GPU
  12times FP64 Tensor Core
  18times FP16 Tensor Core
Multi-core CPU
Notes: Rpeak GPU* : FP64 Tensor Core
V100 – 7.8TFLOPS
A100 – 19.5TFLOPS
K40 – 1.44TLOPS
Raw Peak AI GPU**: FP16 Tensor Core
V100 – 125TFLOPS
A100 – 312TFLOPS
K40 – NONE

## Slide 40: Detail Design
COMING SOON

## Slide 41
HPE Cray EX Cabinet-1
HPE Cray EX Cabinet-2
HPE Cray EX Cabinet-3
HPE Cray EX Cabinet-4
LMN Blade
LMN Blade
LMN Blade
HPC | Cray EX Compute Cabinet Layout

## Slide 42
Cabinet 1
Cabinet 4
Cabinet 2
Cabinet 3
Cray EX - Base Compute Partition (Class 4)
Dragonfly Topology
11 TB/s Injection b/w
6.4 TB/s Global b/w
>50% global b/w taper
Area A
Area B
Compute & Storage Racks
Login, Viz, Specialized Compute & Storage Partition (Class 2)
Bundle Size =4 2.4 TB/s
8 TB/s Injection b/w
5.4 TB/s Global b/w
30m cables
Slingshot Design and Partition